## Slide 1: Processes (Revisited)
Operating Systems

## Slide 2: Processes
A process is a program in execution (It sometimes called a job).
  It is the unit of work in a modern time-sharing system, which allow multiple processes to execute concurrently.
  Q: what is the differences between a process and a program?
As a process executes, it changes state. We can define the following Process States:
  Ready: Process would do something if the CPU was available.
  Running: Process is being executed by the CPU.
  Blocked: Process cannot continue until some event occurs.
If we assume a single CPU, only one process can be running at a time.
  Several may be ready or blocked, and so we need a ready list, and a blocked list.
  If a priority scheme is being used, then a number of ready queues could be used, one for each priority level.

## Slide 3: Process State Transition Diagrams
Processes can move between states as shown...

## Slide 4: Process State Transition Diagrams
The system operates as follows:
  A process initially goes to the back on the ready list.
  Dispatcher takes process at head of ready list and transforms its state to Running.
  Each process is allocated the CPU for a specific interval (quantum).
  A hardware interrupting clock generates an interrupt, returns control to the OS, returns this process’s state to Ready, and makes the first process on the ready list Running.
  The process voluntarily relinquishes the CPU if it initiates an I/O operation. It enters the Blocked state until the operation completes.

## Slide 5: Suspending and Resuming Processes
Processes can be suspended, and later resumed. Suspension involves removing the process from main memory and storing it on secondary storage.
The usual reasons are:
  the process may not be immediately available for execution
  to release some main memory to a process that is ready to execute
  a process may be suspected of causing a problem
  if a process is active only periodically
  user action, eg. for debugging purposes.
  to reduce system load at peak times,
Suspension is usually brief. For longer term suspension, resources should ideally be freed.

## Slide 6: Revised State Transition Diagram
A process in the blocked state is not doing anything, so why not wait until it becomes unblocked and transfer its state to Ready, and then to Suspended Ready?

## Slide 7: The Process Control Block
The PCB is a data structure containing all the information about a process needed by the OS including:
  Current state
  Process ID
  Pointer to parent
  Pointers to children
  Program counter
  Priority
  Pointers to process’s memory
  Pointers to allocated resources
  Register save area
  List of open files
Hardware registers and instructions ensure fast availability of PCB information.

## Slide 8: Operations on Processes
The OS must have the capability of performing the following operations on processes.
  Create (naming; inserting into process table; find priority; create PCB; allocate resources)
  Destroy
  Suspend
  Resume
  Change priority
  Block
  Wakeup
  Dispatch
  Enable intercommunication
  Enable spawning (parent/child relationship)

## Slide 9: Process Switching
A process switch may occur any time that the OS has gained control from the currently running process.
There are three events that may cause the OS to gain control.
  Interrupt. With an ordinary interrupt, control is passed to an interrupt handler, which does some basic housekeeping and then branches to an OS routine that is concerned with the particular type of interrupt that has occured, eg. clock, I/O event, memory fault
  Trap. This relates to an error or exception condition generated within the current process, eg. illegal file access. The OS first determines if the condition is fatal, in which case it is terminated. Otherwise the action depends on the nature of the error (eg. it may simply inform the user)
  Supervisor Call. The OS may be activated by a Supervisor Call from the process, eg. an instruction is executed that requests an I/O operation. This results in a transfer to a routine that is part of the OS code.

## Slide 10: Process Switching
The steps involved in a full process switch are as follows:
  Save the context of the processor (eg program counter and other registers)
  Update the PCB of the process currently running
  move the PCB of this process to the appropriate queue (eg. blocked, suspended)
  Select another process for execution
  Update the PCB of the selected process
  Update memory management data structures
  Restore the context of the processor to that which existed at the time the selected process was last switched out of the running state.